# micROS RT User's Guide
micROS RT, an implementation of ROS 1.x on DDS

Part I What is micROS RT ? Why micROS-RT

MicROS RT (micROS Real-Time) is a modified ROS C++ kernel which adopts OMG's DDS (Data Distribution Systems for Realtime Systems) as its underlying message transfer protocol. DDS is an Object Management Group's standard for pub/sub middleware (http://portals.omg.org/dds/). It supports high-performance, scalable and QoS-assuring message delivery. It has been applied into many industry-level systems.

By replacing the original ROS message protocols (TCPROS & UDPROS) with DDS, we can support a set of advanced features in ROS message delivery process, such as UDP-based multicast and setting the QoS properties (transport priority, latency budget, etc.) of a specific topic. In concrete, we can achieve the benefits as follows.

General benefits
(1) Multicast in message delivery. The DDS middleware will automatically select the multicast protocol when necessary. Therefore, when there are n listeners in a topic (n>=2), you can achieve significant performance benefit.
(2) Robustness in unexpected settings. Since DDS is a mature and industry-level message delivery system, it is behaves better in various complex communications settings. For example, it has better reconnection behavior when dropping out of wireless.

QoS-related benefits
(1) Transport priority and latency budget of a topic. With micROS RT, you can specify the transport priority and latency budget of a topic. It is useful in many real-time settings, such as multi-robot collaboration with limited wireless network bandwidth.
(2) Expected message arriving deadline. With micROS RT, you can set the expected message arriving period as well as the behavior when a message not arriving in this period. It is also useful in real-time settings.
(3) Time-based message filter. You can filter unnecessary messages based on time properties. For example, if you need only update the state of a sensor per minute, you can ignore other redundant messages by simply setting a property while you subscribing the topic.
(4) Other QoS-related features. With micROS RT, you can specify other QoS-related properties provided by the underlying DDS middleware in a simplified way when advertising/subscribing a topic, such as reliability of message delivery, data-centric update, message order method, and message valid period.

Compatibility
(1) Compatibility with existing ROS packages.

In fact, the ROS official has also the plan to integrate ROS 2.0, the next generation of ROS, with DDS (http://design.ros2.org/articles/ros_on_dds.html)